RV Docking Checklist

Thor Serrano 33A-12/24/11

## Park and stabilize:

### Park the RV on as level a surface as possible; make sure slides can open unimpeded.

### Place the transmission in “P” (park) and set the emergency brake.

### While the engine is still cooling down (3 minutes), extend the jacks:

#### If the ground is soft, center wood pads under each stabilizer. If it is sloped, center wood pads under low stabilizer(s). Use a maximum of two under a stabilizer. (Wood pads are located in the forward driver’s-side basement compartment.)

#### Push ON/OFF button on the Electronic Leveling System by the driver’s seat, wait until low voltage light goes off (goose the engine if necessary).

#### Push and hold the AUTO button until the light comes on.

#### The jacks will lower and attempt to level the coach automatically. When the coach is level, the green LEVEL light in the center of the diamond will come on.

#### If the green LEVEL light does not come on, there will be lights flashing to indicate which stabilizer(s) (right/left and front/rear) need additional height. Push RETRACT ALL JACKS twice. (One push shuts off alarm; second push raises the jacks.)

#### When the jacks have retracted, place wood pad(s) under the center of the jack(s) indicated by the flashing lights. (Never put more than 2 pads under any one jack.) If the coach is still not level with 2 pads, push OFF/ON to turn off the stabilizing system and move the coach to ground that is more level and go through this procedure again.

#### With the pads in place, push the AUTO button again to lower the jacks again.

#### Once the green LEVEL light comes on, you are finished leveling. Turn off the ignition.

## After the coach is level:

### Turn off the ignition and move the driver’s seat all the way forward.

### Extend the step by opening the door and then turn off chassis disconnect (by the entry steps at the battery disconnect) and put out the portable step.

### Hook up utilities outside:

#### Power: Check to see that the breakers are off at the park’s outlet; then plug in, using adapters as necessary for amperage. Turn on the park’s breakers. (If you’re not using the park’s power hookup, turn on the inverter at the entry step.)

#### Water: Hook up the hose and fill it with water (flushing it clean in the process), and then connect the other end of the hose to the RV and turn it on, or turn on the water pump. Do not turn on the water pump when using water from an external supply.

#### Sewer: Take off floor drain cover. Wearing gloves, remove the cover;  a small amount of sewage may drain out. Connect the drain hose and pull on the grey water gate valve to open it. DO NOT open the black water gate valve, as sludge will build up in the tanks; only drain the black water tank when it is ¾ full or just before moving the RV. Always close the black water drain valve after draining. Close the grey water valve the day before you move to have water to flush the hose after draining the black water tank.

#### Galley drain (in battery bay, 2nd driver’s side compartment): hook up.

#### Cable: Hook up.

### Get any items out of exterior basement storage compartments; they will be difficult to get at once the slide-outs are extended.

## Back inside:

### Turn on the Inverter (if not on shore power) at the Inverter remote switch by the entry steps.

### Water heater: Bleed air from hot water system (if necessary) by turning on a hot water faucet until air stops coming out. Switch on the water heater at the control panel by pushing WATER HEATER button (gas) or, if connected to park power, the 110V switch.

## Extend the couch slide: (only if RV is level)

### Make sure nothing is in the way to impede movement of the slide inside (both sides) and out:

### Move the passenger’s seat forward and remove items behind the passenger’s seat.

### With no one in the slide area, push and hold the Slide 2 EXTEND button at the control panel over the door until the slide stops moving + 3 seconds.

## Extend the bedroom slide: (only if RV is level)

### Make sure nothing is in the way to impede movement of the slide inside (both sides) and out:

### Push and hold Extend button in the hall outside the bedroom until the slide stops moving + 3 seconds.

## Extend the kitchen/dining slide: (only if RV is level)

### Check outside that there are 3 feet of clearance from the RV to any obstructions and that the water heater exhaust on the left rear side will be 2 feet away from trees or other flammable objects once extended.

### The driver’s seat and items behind the driver’s seat and the area by the bathroom door are clear.

### With no one in the slide area, push and hold the Slide 1 EXTEND button until the slide stops moving + 3 seconds.

## MISC

### Turn refrigerator to AC (switch on door)

### Turn water heater to 110 (switch on control panel over door)

### Black water tank isolation valve is must be closed until the take is 1/3 full.

### To use the generator: at the dashboard, generator or the control panel over the door, push the GENERATOR STOP button and hold until the primed light comes on, then push the GENERATOR START button until the generator starts and the red light stops flashing and stays solid red. To avoid exhaust gas entry into the motor home, keep left and forward windows closed when the generator engine is running

### To turn on furnace or air conditioning outside the bathroom, set the mode to COOL or FURNACE. Set desired temperature. The bedroom thermostat controls only the aft air conditioner; the forward thermostat is for heat in the bedroom and throughout the RV and AC in the front.

### Always open the FAN-TASTIC VENT and turn it on when cooking or showering or mold will occur.

### The awning should be retracted when not in use as a high wind will damage it. If it needs to be rolled up wet, open and dry it at your next opportunity.

Dimensions: Height: 11’5”, Length: 34’3”, Width 8’5” + mirrors.

RV Underway Checklist

Thor Serrano 33A

## Shutdown

### Close and lock all windows and roof vents.

### Lower all antennas.

### Secure the chairs off the floor to the table with bungees and slots in the table support.

### Retract the awning.

### Turn off both electric and gas switches for water heater at the control panel over the door.

### Turn off furnace or air at the thermostats outside the bathroom and in the bedroom.

### Set the refrigerator to gas (if necessary).

### Latch pantry slide, close and latch all drawers and doors.

### Loose items are put away

### Lock shower door closed and close bathroom door.

## Retract the bedroom slide:

### Put away table extension and folding chairs, and anything in the bedroom lower cabinets.

### Check to see that nothing is on the floor between the slide and the bed as the slide goes under the bed.

### Push and hold Side Room RETRACT in the hallway until the slide stops moving + 3 seconds. .

## Outside:

### Bring keys for the compartments with you.

### Disconnects:

#### With gloves on, drain and flush the black water tank first (larger valve), closing the black water tank isolation valve above and left of the Propane tank afterwards.

#### Drain and flush the shower grey water tank. If you close the grey water drain valve ½ day before moving and let water build up in the grey water tank that can serve to flush sewage from the drain hose.

#### Drain and flush the galley grey water tank, drain valve is located at the aft side of the battery compartment.

#### Disconnect and rinse out the drain hose with fresh water and replace it in the storage compartment.

#### Replace the sewage drain cover (which must be on before moving).

#### Rinse the drain area with water from sprayer and wash your hands.

#### Turn off water at spigot and unhook and drain water hose, securing ends of the hose to each other with the pressure regulator in between, to prevent contamination of the hose; Fill the drinking water tank only if you plan to dry camp, no need to carry the extra weight around. Lock the water compartment door closed. Turn on the water pump.

#### Disconnect TV cable and stow in storage compartment.

#### Turn off breakers, disconnect power, and coil up power cable in storage compartment.

### Close all basement doors and the BBQ center, ensuring that the lights are off; lock as necessary.

### Raise and lock the motorcycle lift.

### Check fluid levels. Engine oil, coolant, brakes, transmission, power steering, windshield washer, jack and generator oil and coolant.

## Back inside:

### Put TST in the toilet. Flush toilet for two minutes to insure solids will be under water, important, if the black water tank isolation valve is not closed, this will just fill the crossover piping and never get TST in your tank!

### Pick up and stow away all items from horizontal surfaces and floors, as everything not tied down will be a hazard and damage the coach.

### Check the tank levels; get propane as necessary between campsites.

## Retract kitchen/dining room slide #1:

### Lower the TV with the button to the left of the TV.

### Put the driver’s seat in the driving position with the back upright.

### Close the bathroom door.

### Make sure nothing is in the way to impede movement of the slide including the chairs

### With no one in the slide area, push and hold the bottom of the Slide button 1 at the control panel until the slide is retracted completely + 3 seconds.

## Retract the couch slide #2:

### Put the passenger’s seat in the driving position with the back upright.

### Make sure nothing is in the way to impede movement of the slide:

#### Ottoman & Bed folded up

#### Make sure nothing is fallen by the sides of the bed where the slide retracts.

### With no one in the slide area, push and hold the bottom of Slide button #2 at the control panel until the slide is retracted completely + 3 seconds.

## Raise all of the jacks:

### Connect the chassis battery at the door and start the engine by turning on the ignition switch, wait until the controls boot up and “Wait to Start” light comes on and then goes out (Lower left).Start the engine (the diesel engine needs 5 minutes to warm up before driving, the transmission needs 30 seconds before putting it in drive).

### Push ON/OFF button on the Electronic Leveling system, goose the engine if the low power light is not off.

### Push RETRACT ALL JACKS button; wait until all jacks are up.

### Turn off the jacks.

## Final checks:

### Do an outside walk-around, checking that …

#### All slides are fully retracted against their seals.

#### Jacks are up and pads and wheel chocks stowed.

#### Windows are closed

#### Awning is fully retracted

#### Everything is disconnected and ready for the road.

#### Tow bar and motorcycle lift up and secured.

### Once inside …

#### Lock the door.

#### Turn on automatic step by pushing the top of the POWER STEP button,

#### Disconnect the inverter and insure coach and chassis batters are connected.

## Underway

### Check fuel level, mirrors (Mirror heating), step up (right camera), GPS and levelers up +

### Release emergency break, put it in drive and get underway.