TRAVEL PREPARATION (Draft)

Chassis Checks

Like any vacation trip, pre-planning will pay big dividends. In addition to routine trip preparations such as having newspaper delivery stopped and mail held at the post office, there are now more vehicle-related preparations than there are with an automobile.

• Fluid levels (oil, power steering, radiator, transmission, windshield washer, etc.)

• Belts (tension and condition)

• Battery (electrolyte level if applicable, connections, charge)

• Hoses (clamps tight, condition, leakage)

• Seals, gaskets (leaks)

Exterior Checks

• Tire pressure/condition and lug nut torque

• Headlights, running and safety marker lights including brake and turn signal and also any trailer light connections

• Security of any auxiliary equipment such as TV and awning, etc.

• Windshield wiper blades

• Generator compartment

• Fresh and waste water connections/drains and supplies such as high

pressure hose

• Propane compartment/tank

Undercarriage Checks

• Brakes, including lines, pads/shoes, seals

• Engine area for pan gasket or other leaks

• Anything unusual hanging or tangled with road debris such as tree limbs

• Tank condition (gas, fresh water, waste water)

Operational Checks

• Check operation of all systems, including: Wipers, windshield, horn, brakes, steering, transmission, heater, defroster, air conditioner, and seat adjustment.

• Also idle engine long enough to check cooling system and alternator operation. Be sure to turn on headlights and climate controls to see if alternator handles the additional drain on the electrical system (should not show discharge).

Pre-Trip Checklist

The following checklist will assist your preparing the living quarters for a trip

• In winter make sure that the fresh water tank system is freeze protected.

• Make sure that all storage items are secured and that heavy items are stored low so they don’t fall.

• Check operation of stove and refrigerator.

• Check that you have proper paperwork such as owner’s registration card, vehicle registration, proof of insurance, and valid driver’s license.

• When preparing for your trip, always consider vehicle weight when loading the motor home.

Fluids

Transmission

Allison Approved TES 295 Fluids

Change 150,000 Miles 48 Months 4000 hours

Filter (Control Main & Lube/Aux) 50,000 Miles 24 Months 2000 hours

Maxforce 7 Engine

CJ-4 oil – 10W-30

Radiator

Chevron Texaco Delo Extended Life Coolant