Monthly Storage  (draft)

If not run during the month.

Connect chassis and coach batteries

Start Engine, run for 15 Minutes

Turn on Chassis Air conditioner with vent open (not max AC) fan on high.

Entry door open (or ceiling vent cracked if raining)

Start Generator, run for 15 minutes

Run each Coach A/C one at a time for 5 minutes (inside temp over 40º)

Check desiccant, replace as necessary

Check for water leaks

Prepare for freezing weather if necessary

Turn everything off, close vent and all windows

Open all closets, cabinet doors and drawers.

Disconnect chassis and coach batteries

Lock up

Check tiers, cover exterior vents

Storage of the Motor home

During those periods when the motor home is not in use, care must be taken to ensure moisture sources are addressed. Ideal storage of the motor home would be in an enclosed climate controlled environment. When this is not possible, the following steps should be taken to ensure moisture is controlled:

• Open all closets, cabinet doors and drawers.

• Close all windows and entrance doors.

• Open a vent enough to allow for some limited ventilation air flow, but not so far as to allow snow or rain to enter.

• When storing the motor home high humidity climates (ambient relative humidity is greater than 60% year round), add a dehumidifier

• Turn off all water sources.

• Turn off all combustion appliances.

• Drain all holding tanks.

• Drain the water heater.

STORAGE PREPARATION

When storing the motor home for the winter (or other extreme conditions), certain precautions need to be made to protect it until you open it again for use. Make sure to talk with your local dealer concerning any special requirements for storage in your particular geographic area. The following steps are general, and your dealer can help you choose those that are most appropriate for your needs.

1. Make sure to park the motor home on a level surface.

2. Make sure to winterize the chassis as outlined in the chassis owner’s manual, and also the 120V generator (If so equipped) as outlined in the generator owner’s manual.

3. Clean the motor home thoroughly, both inside and out, as previously outlined including the refrigerator.

4. Make sure all electrical switches and appliances are turned off.

5. Close all the drapes and curtains, and protect the curtains from sun fading by placing foil, or paper between the windows and the screens.

6. Make sure all windows, doors, and vents are closed securely. Cover exterior vents on appliances to prevent moisture and insects from entering during storage.

7. Check the interior of the motor home periodically while in storage to make sure leaks have not developed, or condensation formed that can cause damage to interior components. Condensation can most readily be observed as moisture accumulation on windows and mirrors. To reduce condensation, make sure to air the motor home out occasionally during storage.

8. Be sure that both the chassis and auxiliary batteries have the proper electrolyte level and that they are fully charged (12.7 Volts). A discharged battery will freeze and crack the case, ruining the battery. In storage, a battery will lose charge gradually over a 30 to 45 day period, even when disconnected by use of the battery disconnect switch. We recommend that at least monthly the batteries be checked for charge. If the charge is 80% (12.5 Volts) or less, it must be recharged.

• You may wish to remove the batteries from the motor home and store them in a heated area. However, even when warm, the battery charge level must still be maintained, a warm battery accepts charge much more readily however, than a cold one.

• Make sure to follow all precautions associated with battery care and maintenance outlined in the electrical section of this manual.

9. Store with as much fuel as possible in the fuel tank to limit condensation buildup.

10. Check engine coolant, making sure antifreeze is sufficient for local temperature extremes.

11. Make sure the tires are inflated to correct pressures.

12. Store the windshield wiper arms and blades inside the motor home.

13. Let the engine run for a period of time until it is warm. Change the oil and oil filter.

14. Run the air conditioner during this final engine warm up to make sure the compressor seal is lubricated.

15. If snow accumulates on the motor home, try to remove it as often as you can.

16. A primary concern when winterizing the motor home is to make sure the water systems are protected against damage caused by freezing. Follow the water system winterizing procedure outlined in the Water and Drainage section of this manual (check the Index for location).

Note: Be sure to read the rest of this manual, and follow any additional information on storage, cleaning, and winterizing procedures.